## Slide 1
ABC CHEMISTRY
Mr. Aniket Bhardwaj · 15+ Years Mentorship
Analytical Chemistry (Inorganic)
Premium CSIR-NET PYQ Book
30 Previous-Year Questions · 24 with verified answers · Distractor Analysis
3-Slide Solutions
Distractor Analysis
Exam Tricks
Revision Sheets
CSIR-NET · GATE · IIT-JAM — 1 Topics · 30 Real PYQs
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Mr. Aniket Bhardwaj
@abcchemistry24
Instagram · YouTube · Facebook

## Slide 2
Course Contents
1 Topics · 30 PYQs
1
Analytical Chemistry (Inorganic) – General
30 Qs E 18 · M 11 · H 1
100%
Legend: E Easy M Medium H Hard · % = exam weightage (share of the chapter)
( Mr. Aniket Bhardwaj By ABC Chemistry )

## Slide 3
TOPIC 1
Analytical Chemistry (Inorganic) – General
30 questions · Easy 18 | Medium 11 | Hard 1 · PYQ frequency: Very High
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427

## Slide 4
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2013
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 1 of 30
Q1
In the atomic absorption spectroscopic estimation of Fe(III) using O₂ / H₂ flame, the absorbance decreases with the addition of
A
CO₃²⁺
B
SO₄²⁻
C
EDTA
D
Cl⁻
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q1 · Question

## Slide 5
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2013
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 1 of 30
✓
Correct Answer B SO₄²⁻
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Sulfate (like phosphate) forms thermally stable, poorly atomised iron salts in the cooler O₂/H₂ flame — a chemical interference that lowers the absorbance. EDTA and Cl⁻ give volatile species and do not suppress it.
Therefore the answer is (B).
FINAL: (B) SO₄²⁻
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q1 · Answer & Explanation

## Slide 6
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2013
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 1 of 30
Why the Other Options Are Wrong
Correct answer: B
A
CO₃²⁺
Why (B) is the key — Sulfate (like phosphate) forms thermally stable, poorly atomised iron salts in the cooler O₂/H₂ flame — a chemical interference that lowers the absorbance. EDTA and Cl⁻ give volatile species and do not suppress it.
C
EDTA
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
Cl⁻
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q1 · Distractor Analysis

## Slide 7
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2014
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 2 of 30
Q2
The gas commonly used in generating plasma in Inductively Coupled Plasma Atomic Emission Spectroscopy (ICPAES) is:
A
Argon
B
Carbon dioxide
C
Nitrous oxide
D
hydrogen
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q2 · Question

## Slide 8
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2014
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 2 of 30
✓
Correct Answer A Argon
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
For ICP-OES and ICP_MS argon is most suitable gas to generate plasma. A number of gases cane be used to produce plasma, like Ar, Ne, N2, O2, H2 , air and mixture of gases. The physical properties of the gases play a decisive role in this regard. Such important properties are ionization and dissociation energy, thermal conductivity, atomic weight and chemical reactivity. Argon belongs to the group of inert gases. It means that it does not react with the material during production of plasma. Its atomic weight - the highest among all plasma gases and it generates high kinetic energy of the plasma beam. Due to its low ionization potential argon is excellently suitable for generating the plasma beam. However, argon has a low thermal conductivity and a low thermal capacity which limits its application is some specific areas only. Explanation as extracted from the printed page; notation may be imperfect.
Therefore the answer is (A).
FINAL: (A) Argon
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q2 · Answer & Explanation

## Slide 9
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2014
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 2 of 30
Why the Other Options Are Wrong
Correct answer: A
B
Carbon dioxide
Why (A) is the key — For ICP-OES and ICP_MS argon is most suitable gas to generate plasma. A number of gases cane be used to produce plasma, like Ar, Ne, N2, O2, H2 , air and mixture of gases. The physical properties of the gases play a decisive role in this regard. Such important properties are ionization and dissociation energy, thermal conductivity, atomic weight and chemical reactivity. Argon belongs to the group of inert gases. It means that it does not react with the material during production of plasma. Its atomic weight - the highest among all plasma gases and it generates high kinetic energy of the plasma beam. Due to its low ionization potential argon is excellently suitable for generating the plasma beam. However, argon has a low thermal conductivity and a low thermal capacity which limits its application is some specific areas only. Explanation as extracted from the printed page; notation may be imperfect.
C
Nitrous oxide
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
hydrogen
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q2 · Distractor Analysis

## Slide 10
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 3 of 30
Q3
Correct statement for coulometry is 1. it is based on Faraday's law of electrolysis 2. It is a type of voltammetry 3. it is based on Ohm's law 4. it uses ion selective electrode
(Numerical answer type — write the value.)
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
Coulometry measures the quantity of charge consumed (Q = nFN) and relates it to the amount of analyte through Faraday's laws of electrolysis — an absolute method needing no calibration.
ANSWER: (A)
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q3 · Practice Question

## Slide 11
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 4 of 30
Q4
The calibration curve in spectrofluorimetric analysis becomes non-linear when 1. molecular weight of analyte is high 2. intensity of light source is high 3. concentration of analyte is high 4. molar absorptivity of analyte is high
(Numerical answer type — write the value.)
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
SELF-PRACTICE answer on record: (C) — options were not printed in the source.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q4 · Practice Question

## Slide 12
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 5 of 30
Q5
The calibration curve in spectrofluorimetric analysis becomes non-linear when
A
molecular weight of analyte is high
B
intensity of light source is high
C
concentration of analyte is high
D
molar absorptivity of analyte is high
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q5 · Question

## Slide 13
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 5 of 30
✓
Correct Answer C concentration of analyte is high
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
At high analyte concentration the inner-filter effect (self-absorption of excitation/emission light) and self-quenching make F non-linear in c; the linear law holds only for absorbance < ~0.05. (Bank key (a) was wrong — corrected.)
Therefore the answer is (C).
FINAL: (C) concentration of analyte is high
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q5 · Answer & Explanation

## Slide 14
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 5 of 30
Why the Other Options Are Wrong
Correct answer: C
A
molecular weight of analyte is high
Why (C) is the key — At high analyte concentration the inner-filter effect (self-absorption of excitation/emission light) and self-quenching make F non-linear in c; the linear law holds only for absorbance < ~0.05. (Bank key (a) was wrong — corrected.)
B
intensity of light source is high
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
molar absorptivity of analyte is high
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q5 · Distractor Analysis

## Slide 15
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2016
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 6 of 30
Q6
The primary analytical method (not using a reference) is: 1) inductively coupled plasma emission spectrometry 2) energy dispersive X-ray fluorescence spectrometry 3) anodic stripping voltammetry 4) isotopic dilution mass spectrometry
(Numerical answer type — write the value.)
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
Isotope-dilution mass spectrometry is a primary (definitive) method: the spike of enriched isotope is the internal reference and the result follows from first principles. ICP-OES, XRF and stripping voltammetry need external calibration standards.
ANSWER: (D)
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q6 · Practice Question

## Slide 16
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2016
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 7 of 30
Q7
The primary analytical method (not using a reference) is: (a) inductively coupled plasma emission spectrometry (c) anodic stripping voltammetry (d) isotopic dilution mass spectrometry (b) energy dispersive X-ray fluorescence spectrometry
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
SELF-PRACTICE answer on record: (D) — options were not printed in the source.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q7 · Practice Question

## Slide 17
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2017
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 8 of 30
Q8
To determine the bond parameters at 25Â°C, electron diffraction is generally unsuitable for both
A
O₃ and NO₂
B
Sulfur and dry ice
C
NO₂ and sulphur
D
O₃ and dry ice
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q8 · Question

## Slide 18
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2017
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 8 of 30
✓
Correct Answer B Sulfur and dry ice
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Gas-phase electron diffraction needs a vapour; at 25 °C sulfur and dry ice (solid CO₂) are solids, whereas O₃ and NO₂ are gases.
Therefore the answer is (B).
FINAL: (B) Sulfur and dry ice
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q8 · Answer & Explanation

## Slide 19
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2017
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 8 of 30
Why the Other Options Are Wrong
Correct answer: B
A
O₃ and NO₂
Why (B) is the key — Gas-phase electron diffraction needs a vapour; at 25 °C sulfur and dry ice (solid CO₂) are solids, whereas O₃ and NO₂ are gases.
C
NO₂ and sulphur
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
O₃ and dry ice
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q8 · Distractor Analysis

## Slide 20
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2017
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 9 of 30
Q9
The peak area of differential thermal analysis curve is proportional to one or more of the following A. mass loss B. mass of the sample C. heat of decomposition / phase change The correct answer is:
A
A only
B
B only
C
A and C
D
B and C
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q9 · Question

## Slide 21
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2017
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 9 of 30
✓
Correct Answer D B and C
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
The DTA peak area is proportional to the mass of the sample and to the enthalpy of the decomposition or phase change (B and C); it does not measure mass loss (that is TGA).
Therefore the answer is (D).
FINAL: (D) B and C
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q9 · Answer & Explanation

## Slide 22
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2017
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 9 of 30
Why the Other Options Are Wrong
Correct answer: D
A
A only
Why (D) is the key — The DTA peak area is proportional to the mass of the sample and to the enthalpy of the decomposition or phase change (B and C); it does not measure mass loss (that is TGA).
B
B only
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
C
A and C
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q9 · Distractor Analysis

## Slide 23
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 10 of 30
Q10
In spectrofluorimetric determination in solution
A
absorbance of analyte solution is kept near to 0.05
B
oxygen is eradicated from solution
C
pH of solution is controlled
D
wavelength of incident light is always above 400 nm Correct from the above is (1)A, B and D (2)B, C and D (3)A, B and C (4)A, C and D
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q10 · Question

## Slide 24
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 10 of 30
✓
Correct Answer C pH of solution is controlled
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
(a) In spectrofluorimetry the wavelength of incident light can range from 200 nm to 900 nm. (b) Intensity and colour of the fluorescence of many substance depends upon the pH of solutions. (c) Since, presence of O2 decreases the fluorescence, thus oxygen is eradicated from the solution. (d) In flourimetry absorbance of analyte solution is generally kept near to 0.05. Explanation as extracted from the printed page; notation may be imperfect.
Therefore the answer is (C).
FINAL: (C) pH of solution is controlled
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q10 · Answer & Explanation

## Slide 25
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 10 of 30
Why the Other Options Are Wrong
Correct answer: C
A
absorbance of analyte solution is kept near to 0.05
Why (C) is the key — (a) In spectrofluorimetry the wavelength of incident light can range from 200 nm to 900 nm. (b) Intensity and colour of the fluorescence of many substance depends upon the pH of solutions. (c) Since, presence of O2 decreases the fluorescence, thus oxygen is eradicated from the solution. (d) In flourimetry absorbance of analyte solution is generally kept near to 0.05. Explanation as extracted from the printed page; notation may be imperfect.
B
oxygen is eradicated from solution
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
wavelength of incident light is always above 400 nm Correct from the above is (1)A, B and D (2)B, C and D (3)A, B and C (4)A, C and D
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q10 · Distractor Analysis

## Slide 26
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 11 of 30
Q11
The pair of light source and atomizer resulting highest sensitivity to atomic absorption spectrometric measurement is:
A
Hg lamp, nitric oxide flame
B
Hg lamp, graphite furnace
C
Hollow cathode lamp, graphite furnace
D
Hollow cathode lamp; acetylene-nitric oxide flame
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q11 · Question

## Slide 27
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 11 of 30
✓
Correct Answer C Hollow cathode lamp, graphite furnace
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
A hollow-cathode lamp with a graphite furnace gives the highest AAS sensitivity (c).
Therefore the answer is (C).
FINAL: (C) Hollow cathode lamp, graphite furnace
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q11 · Answer & Explanation

## Slide 28
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 11 of 30
Why the Other Options Are Wrong
Correct answer: C
A
Hg lamp, nitric oxide flame
Why (C) is the key — A hollow-cathode lamp with a graphite furnace gives the highest AAS sensitivity (c).
B
Hg lamp, graphite furnace
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
Hollow cathode lamp; acetylene-nitric oxide flame
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q11 · Distractor Analysis

## Slide 29
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 12 of 30
Q12
Inspectrofluorimetric determination in solution A. absorbance of analyte solution is kept near to 0.05 B. oxygen is eradicated from solution C. pH of solution is controlled D. wavelength of incident light is always above 400 nm
A
A, B and D
B
B, C and D
C
A, B and C
D
A, C and D
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q12 · Question

## Slide 30
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 12 of 30
✓
Correct Answer C A, B and C
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
For spectrofluorimetry, absorbance is kept low ( 0.05) to avoid inner-filter effects, quenching O₂ is removed, and pH is controlled. The excitation λ is chosen at the absorption band, not necessarily above 400 nm. A, B and C (c).
Therefore the answer is (C).
FINAL: (C) A, B and C
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q12 · Answer & Explanation

## Slide 31
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-DEC 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 12 of 30
Why the Other Options Are Wrong
Correct answer: C
A
A, B and D
Why (C) is the key — For spectrofluorimetry, absorbance is kept low ( 0.05) to avoid inner-filter effects, quenching O₂ is removed, and pH is controlled. The excitation λ is chosen at the absorption band, not necessarily above 400 nm. A, B and C (c).
B
B, C and D
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
A, C and D
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q12 · Distractor Analysis

## Slide 32
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2011
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 13 of 30
Q13
Thermometric titration gives best results when A. |Δ H| is high B. Δ G<0 C. Heat of mixing of titrant with titrant is high D. Titrant is used as dilute solution The answer is
A
A and B
B
B and C
C
C and D
D
A and D
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q13 · Question

## Slide 33
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2011
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 13 of 30
✓
Correct Answer A A and B
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Thermometric titration follows the temperature change of the reaction, so it works best when the reaction enthalpy is large (|ÎH| high).
Therefore the answer is (A).
FINAL: (A) A and B
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q13 · Answer & Explanation

## Slide 34
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2011
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 13 of 30
Why the Other Options Are Wrong
Correct answer: A
B
B and C
Why (A) is the key — Thermometric titration follows the temperature change of the reaction, so it works best when the reaction enthalpy is large (|ÎH| high).
C
C and D
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
A and D
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q13 · Distractor Analysis

## Slide 35
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2011
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 14 of 30
Q14
The FALSE statement for a polarographic measurement procedure is:
A
O₂ is removed
B
Dropping mercury electrode is working electrode
C
Id is proportional to concentration of electro active species
D
Residual current is made zero by adding supporting electrolyte
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q14 · Question

## Slide 36
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2011
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 14 of 30
✓
Correct Answer D Residual current is made zero by adding supporting electrolyte
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
The supporting electrolyte suppresses the migration current, not the residual current; the residual (charging) current remains and is corrected for. The other statements are true.
Therefore the answer is (D).
FINAL: (D) Residual current is made zero by adding supporting electrolyte
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q14 · Answer & Explanation

## Slide 37
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2011
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 14 of 30
Why the Other Options Are Wrong
Correct answer: D
A
O₂ is removed
Why (D) is the key — The supporting electrolyte suppresses the migration current, not the residual current; the residual (charging) current remains and is corrected for. The other statements are true.
B
Dropping mercury electrode is working electrode
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
C
Id is proportional to concentration of electro active species
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q14 · Distractor Analysis

## Slide 38
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2014
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 15 of 30
Q15
The use of dynamic inert atmosphere in thermogravimetric analysis (TGA): (1) decreases decomposition temperature (2) decrease weight loss (3) reduces rate of decomposition (4) increases weight loss
A
decreases decomposition temperature
B
decrease weight loss
C
reduces rate of decomposition
D
increases weight loss
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q15 · Question

## Slide 39
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2014
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 15 of 30
✓
Correct Answer D increases weight loss
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
In thermogravimetric analysis (TGA) use of dynamic innert atmosphere is decrease with respect to temperature. Explanation as extracted from the printed page; notation may be imperfect.
Therefore the answer is (D).
FINAL: (D) increases weight loss
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q15 · Answer & Explanation

## Slide 40
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2014
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 15 of 30
Why the Other Options Are Wrong
Correct answer: D
A
decreases decomposition temperature
Why (D) is the key — In thermogravimetric analysis (TGA) use of dynamic innert atmosphere is decrease with respect to temperature. Explanation as extracted from the printed page; notation may be imperfect.
B
decrease weight loss
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
C
reduces rate of decomposition
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q15 · Distractor Analysis

## Slide 41
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2014
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 16 of 30
Q16
The correct statements for hollow cathode lamp (HCL) from the following are: (A) HCL is suitable for atomic absorption spectroscopy (AAS) (B) lines emitted from HCL are very narrow (C) the hardening of lamp makes it unsuitable for AAS (D) transition elements used in lamps have short life
A
A, B and C
B
B, C and D
C
C, D and A
D
D, A and B
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q16 · Question

## Slide 42
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2014
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 16 of 30
✓
Correct Answer A A, B and C
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
The HCL is the standard AAS source and emits very narrow lines. Hardening (gas clean-up) degrades a lamp. Chapter key (a).
Therefore the answer is (A).
FINAL: (A) A, B and C
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q16 · Answer & Explanation

## Slide 43
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2014
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 16 of 30
Why the Other Options Are Wrong
Correct answer: A
B
B, C and D
Why (A) is the key — The HCL is the standard AAS source and emits very narrow lines. Hardening (gas clean-up) degrades a lamp. Chapter key (a).
C
C, D and A
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
D, A and B
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q16 · Distractor Analysis

## Slide 44
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2015
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 17 of 30
Q17
The pair of light source and atomizer resulting highest sensitivity to atomic absorption spectrometric measurement is: (1) Hg lamp, nitric oxide flame (2) Hg lamp, graphite furnace (3) Hollow cathode lamp, graphite furnace (4)Hollow cathode lamp; acetylene-nitric oxide flame
A
1 and 2
B
2 and 3
C
1 and 3
D
3 only
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q17 · Question

## Slide 45
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2015
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 17 of 30
✓
Correct Answer C 1 and 3
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Increase of intensity of light used increases fluorescence as the fluorescence life-time increases. Molar absorptivity increases absorbance which further enhances fluorescence. CSIR DEC 2014 Explanation as extracted from the printed page; notation may be imperfect.
Therefore the answer is (C).
FINAL: (C) 1 and 3
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q17 · Answer & Explanation

## Slide 46
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2015
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 17 of 30
Why the Other Options Are Wrong
Correct answer: C
A
1 and 2
Why (C) is the key — Increase of intensity of light used increases fluorescence as the fluorescence life-time increases. Molar absorptivity increases absorbance which further enhances fluorescence. CSIR DEC 2014 Explanation as extracted from the printed page; notation may be imperfect.
B
2 and 3
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
3 only
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q17 · Distractor Analysis

## Slide 47
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 18 of 30
Q18
Considering the following parameters with reference to the fluorescence of a solution: 1. Molar absorptivity of fluorescent molecule 2. Intensity of light source used for excitation 3. Dissolved oxygen The correct answer for the enhancement of fluorescence with the increase in these parameters is/are
A
1 and 2
B
2 and 3
C
1 and 3
D
3 only
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q18 · Question

## Slide 48
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 18 of 30
✓
Correct Answer A 1 and 2
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Fluorescence intensity F = 2.303 φ I₀ ε b c for dilute solutions: it rises with the molar absorptivity (1) and the source intensity (2). Dissolved O₂ (3) is a quencher and lowers fluorescence.
Therefore the answer is (A).
FINAL: (A) 1 and 2
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q18 · Answer & Explanation

## Slide 49
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2015
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 18 of 30
Why the Other Options Are Wrong
Correct answer: A
B
2 and 3
Why (A) is the key — Fluorescence intensity F = 2.303 φ I₀ ε b c for dilute solutions: it rises with the molar absorptivity (1) and the source intensity (2). Dissolved O₂ (3) is a quencher and lowers fluorescence.
C
1 and 3
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
3 only
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q18 · Distractor Analysis

## Slide 50
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2016
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 19 of 30
Q19
Decomposition temperature of CaCO₃ in thermogravimetric analysis will be highest in dynamic atmosphere of:
A
nitrogen
B
synthesis gas
C
1: 1 mixture of O₂ and CO
D
water gas
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q19 · Question

## Slide 51
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2016
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 19 of 30
✓
Correct Answer C 1: 1 mixture of O₂ and CO
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
An O₂/CO mixture burns to CO₂; a CO₂-rich atmosphere suppresses CaCO₃ ⇌ CaO + CO₂ and raises the decomposition temperature most (c).
Therefore the answer is (C).
FINAL: (C) 1: 1 mixture of O₂ and CO
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q19 · Answer & Explanation

## Slide 52
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2016
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 19 of 30
Why the Other Options Are Wrong
Correct answer: C
A
nitrogen
Why (C) is the key — An O₂/CO mixture burns to CO₂; a CO₂-rich atmosphere suppresses CaCO₃ ⇌ CaO + CO₂ and raises the decomposition temperature most (c).
B
synthesis gas
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
water gas
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q19 · Distractor Analysis

## Slide 53
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2017
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 20 of 30
Q20
Identify the correct statement(s) for phosphorimetric measurement from the following: A. It is done after a time delay when fluorescence, if present becomes negligible B. Immobilization of analyte increases phosphorescence. C. Phosphorescence decreases in the presence of heavy atoms
A
A only
B
A and B
C
A and C
D
B and C
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q20 · Question

## Slide 54
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2017
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 20 of 30
✓
Correct Answer B A and B
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Phosphorescence is read after a delay when fluorescence has died (A true); immobilising the analyte (frozen matrix, adsorption) suppresses non-radiative decay and raises it (B true); heavy atoms increase intersystem crossing and enhance, not decrease, phosphorescence (C false). A and B.
Therefore the answer is (B).
FINAL: (B) A and B
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q20 · Answer & Explanation

## Slide 55
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2017
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 20 of 30
Why the Other Options Are Wrong
Correct answer: B
A
A only
Why (B) is the key — Phosphorescence is read after a delay when fluorescence has died (A true); immobilising the analyte (frozen matrix, adsorption) suppresses non-radiative decay and raises it (B true); heavy atoms increase intersystem crossing and enhance, not decrease, phosphorescence (C false). A and B.
C
A and C
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
B and C
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q20 · Distractor Analysis

## Slide 56
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2017
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 21 of 30
Q21
Identify correct statements from the following: A. Area of differential thermal analysis peak is proportional to amount of sample. B. Area of differential thermogravimetric analysis curve is proportional to mass loss. C. Phase transition cannot be studied, with differential scanning calorimetry. D. Simultaneous determination of two metal ions is possible with thermogravimetric analysis.
A
A, B and C
B
A, B and D
C
B, C and D
D
A, C and D
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q21 · Question

## Slide 57
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2017
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 21 of 30
✓
Correct Answer B A, B and D
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
The DTA peak area is proportional to the amount of sample, the DTG curve area to the mass lost, and TGA can determine two metals (e.g. Ca/Mg oxalates) at once. DSC is routinely used for phase transitions, so C is false. A, B and D (b).
Therefore the answer is (B).
FINAL: (B) A, B and D
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q21 · Answer & Explanation

## Slide 58
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2017
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 21 of 30
Why the Other Options Are Wrong
Correct answer: B
A
A, B and C
Why (B) is the key — The DTA peak area is proportional to the amount of sample, the DTG curve area to the mass lost, and TGA can determine two metals (e.g. Ca/Mg oxalates) at once. DSC is routinely used for phase transitions, so C is false. A, B and D (b).
C
B, C and D
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
A, C and D
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q21 · Distractor Analysis

## Slide 59
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2018
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 22 of 30
Q22
Height equivalent to theoretical plate (HETP) in gas liquid chromatography depends Significantly on which of the following? (A) Temperature of column (B) Velocity of carrier gas (C) Packing of column (D) Column material
A
A, B and C
B
C and D
C
B, C and D
D
A and C
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q22 · Question

## Slide 60
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2018
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 22 of 30
✓
Correct Answer A A, B and C
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
By the van Deemter equation, HETP depends on carrier-gas velocity, column packing (particle size, eddy diffusion) and temperature (diffusion coefficients, mass transfer). A, B and C (a).
Therefore the answer is (A).
FINAL: (A) A, B and C
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q22 · Answer & Explanation

## Slide 61
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2018
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 22 of 30
Why the Other Options Are Wrong
Correct answer: A
B
C and D
Why (A) is the key — By the van Deemter equation, HETP depends on carrier-gas velocity, column packing (particle size, eddy diffusion) and temperature (diffusion coefficients, mass transfer). A, B and C (a).
C
B, C and D
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
A and C
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q22 · Distractor Analysis

## Slide 62
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 23 of 30
Q23
Incorrect statement for amperometric titration is
A
it is based on measurement of diffusion current
B
its sensitivity is always higher than those of spectrophotometric titrations
C
it does not generally require an indicator
D
it requires inert atmosphere (N₂/Ar)
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q23 · Question

## Slide 63
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 23 of 30
✓
Correct Answer B its sensitivity is always higher than those of spectrophotometric titrations
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Amperometric titrations monitor the limiting (diffusion) current, need no indicator, and often need deaeration when reductions are followed. The false (absolute) claim is that their sensitivity is always higher than spectrophotometric titrations. (Bank key (d) — verify; dead-stop/biamperometric titrations do not need inert atmosphere.)
Therefore the answer is (B).
FINAL: (B) its sensitivity is always higher than those of spectrophotometric titrations
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q23 · Answer & Explanation

## Slide 64
ABC CHEMISTRY
Mr. Aniket Bhardwaj
CSIR-JUNE 2019
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 23 of 30
Why the Other Options Are Wrong
Correct answer: B
A
it is based on measurement of diffusion current
Why (B) is the key — Amperometric titrations monitor the limiting (diffusion) current, need no indicator, and often need deaeration when reductions are followed. The false (absolute) claim is that their sensitivity is always higher than spectrophotometric titrations. (Bank key (d) — verify; dead-stop/biamperometric titrations do not need inert atmosphere.)
C
it does not generally require an indicator
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
it requires inert atmosphere (N₂/Ar)
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q23 · Distractor Analysis

## Slide 65
ABC CHEMISTRY
Mr. Aniket Bhardwaj
GATE
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 24 of 30
Q24
In atomic absorption spectroscopy, the atomization process utilizes
A
flame
B
electric field
C
magnetic field
D
electron beam
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q24 · Question

## Slide 66
ABC CHEMISTRY
Mr. Aniket Bhardwaj
GATE
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 24 of 30
✓
Correct Answer A flame
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
AAS requires free ground-state atoms: the sample is aspirated into an air–acetylene or N₂O–acetylene flame (or a graphite furnace) where it is desolvated, vaporised and atomised.
Therefore the answer is (A).
FINAL: (A) flame
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q24 · Answer & Explanation

## Slide 67
ABC CHEMISTRY
Mr. Aniket Bhardwaj
GATE
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 24 of 30
Why the Other Options Are Wrong
Correct answer: A
B
electric field
Why (A) is the key — AAS requires free ground-state atoms: the sample is aspirated into an air–acetylene or N₂O–acetylene flame (or a graphite furnace) where it is desolvated, vaporised and atomised.
C
magnetic field
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
electron beam
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q24 · Distractor Analysis

## Slide 68
ABC CHEMISTRY
Mr. Aniket Bhardwaj
GATE
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 25 of 30
Q25
On heating a sample of 25 mg hydrated compound (molecular weight = 250 g/mol) in thermogravimetric analysis, 16 mg of dehydrated compound remains. The number of water molecules lost per molecule of hydrated compound is ____. (Molecular weight of water = 18 g/mol)
(Numerical answer type — write the value.)
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
Mass lost = 25 − 16 = 9 mg water = 0.5 mmol. Compound = 25/250 = 0.1 mmol → 0.5/0.1 = 5 H₂O per formula unit.
ANSWER: 5
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q25 · Practice Question

## Slide 69
ABC CHEMISTRY
Mr. Aniket Bhardwaj
GATE
MCQ
Hard
Analytical Chemistry (Inorganic) – General
Question 26 of 30
Q26
The quantity of the cobalt ore [Co₃(AsO₄)₂ · H₂O] required to obtain 1 kg of cobalt (rounded off to two decimal places) is ____ kg. [Atomic Wt. of Co = 59, As = 75, O = 16, H = 1]
(Numerical answer type — write the value.)
QUESTION INSIGHTS
ESTIMATED TIME
3–5 min
DIFFICULTY
Hard
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★★
EXPECTED LEVEL
Part C (high merit)
MEMORY HOOK
M[Co₃(AsO₄)₂·H₂O] = 3(59) + 2(75 + 64) + 18 = 473. Co content = 177/473 = 37.4 % → ore needed = 1/0.374 = 2.67 kg.
ANSWER: 2.67 kg
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q26 · Practice Question

## Slide 70
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 27 of 30
Q27
The indicator phenolphthalein changes colour at pH sim 9. This indicator is NOT suitable for accurate determination of the end point in the titration of
A
CH₃ COOH with NaOH
B
HCl with NH₄ OH
C
HCl with NaOH
D
HCl with KOH
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q27 · Question

## Slide 71
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 27 of 30
✓
Correct Answer B HCl with NH₄ OH
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
HCl vs NH₄OH (weak base) has its equivalence point near pH 5; phenolphthalein changes at pH ≈ 9 and would give a late, indistinct end point. The other three titrations pass through pH 9 at the steep part of the curve. Chapter list · Next in chapter →
Therefore the answer is (B).
FINAL: (B) HCl with NH₄ OH
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q27 · Answer & Explanation

## Slide 72
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 27 of 30
Why the Other Options Are Wrong
Correct answer: B
A
CH₃ COOH with NaOH
Why (B) is the key — HCl vs NH₄OH (weak base) has its equivalence point near pH 5; phenolphthalein changes at pH ≈ 9 and would give a late, indistinct end point. The other three titrations pass through pH 9 at the steep part of the curve. Chapter list · Next in chapter →
C
HCl with NaOH
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
HCl with KOH
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q27 · Distractor Analysis

## Slide 73
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 28 of 30
Q28
In ammonical buffer, oxine (8-hydroxyquinoline) forms yellow precipitate with
A
Mg(II)
B
Ca(II)
C
Ba(II)
D
Sr(II)
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q28 · Question

## Slide 74
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 28 of 30
✓
Correct Answer A Mg(II)
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
In ammoniacal buffer oxine precipitates Mg(II) as yellow Mg(oxinate)₂; Ca, Sr, Ba are not precipitated (a).
Therefore the answer is (A).
FINAL: (A) Mg(II)
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q28 · Answer & Explanation

## Slide 75
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 28 of 30
Why the Other Options Are Wrong
Correct answer: A
B
Ca(II)
Why (A) is the key — In ammoniacal buffer oxine precipitates Mg(II) as yellow Mg(oxinate)₂; Ca, Sr, Ba are not precipitated (a).
C
Ba(II)
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
D
Sr(II)
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q28 · Distractor Analysis

## Slide 76
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 29 of 30
Q29
In the measurement of hardness of water by complexometric titration, identify P and Q in the following equation. [P]⁻ & + & [H₂Y]²⁻ & → & [Q]²⁻ & + & [HIn]²⁻ + H⁺ red & & colourless & & colourless & & blue
A
P=MgY, Q=MgIn
B
P=MgY₂, Q=MgIn₂
C
P=MgIn₂, Q=MgY₂
D
P=MgIn, Q=MgY
QUESTION INSIGHTS
ESTIMATED TIME
2–3 min
DIFFICULTY
Medium
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★★☆
EXPECTED LEVEL
Part B / Part C
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q29 · Question

## Slide 77
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 29 of 30
✓
Correct Answer D P=MgIn, Q=MgY
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
With Eriochrome Black T: [MgIn]⁻ (red) + H₂Y²⁻ → [MgY]²⁻ (colourless) + HIn²⁻ (blue) + H⁺ — P = MgIn, Q = MgY (d).
Therefore the answer is (D).
FINAL: (D) P=MgIn, Q=MgY
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q29 · Answer & Explanation

## Slide 78
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Medium
Analytical Chemistry (Inorganic) – General
Question 29 of 30
Why the Other Options Are Wrong
Correct answer: D
A
P=MgY, Q=MgIn
Why (D) is the key — With Eriochrome Black T: [MgIn]⁻ (red) + H₂Y²⁻ → [MgY]²⁻ (colourless) + HIn²⁻ (blue) + H⁺ — P = MgIn, Q = MgY (d).
B
P=MgY₂, Q=MgIn₂
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
C
P=MgIn₂, Q=MgY₂
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q29 · Distractor Analysis

## Slide 79
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 30 of 30
Q30
Indicator used in redox titration is
A
Eriochrome black T
B
Methyl orange
C
Phenolphthalein
D
Methylene blue
QUESTION INSIGHTS
ESTIMATED TIME
1–1.5 min
DIFFICULTY
Easy
CONCEPT TESTED
Analytical Chemistry (Inorganic) – General
PYQ FREQUENCY
Very High · 15 papers
REVISION PRIORITY
★★★☆☆
EXPECTED LEVEL
Part B
MEMORY HOOK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q30 · Question

## Slide 80
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 30 of 30
✓
Correct Answer D Methylene blue
CONCEPT
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
↓
LOGIC / WORKING
Methylene blue is a redox indicator (blue ⇌ colourless leuco form). Eriochrome black T is a metal-ion indicator; methyl orange and phenolphthalein are acid–base indicators.
Therefore the answer is (D).
FINAL: (D) Methylene blue
SHORTCUT / EXAM TRICK
Mixtures: measure A at two wavelengths and solve two Beer's-law equations.
COMMON MISTAKE
Using %T in place of absorbance; confusing equivalence point with end point.
EXAM TIP
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MEMORY TRICK
'A = εcl — Absorbance Equals ε·c·l'.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q30 · Answer & Explanation

## Slide 81
ABC CHEMISTRY
Mr. Aniket Bhardwaj
IIT-JAM
MCQ
Easy
Analytical Chemistry (Inorganic) – General
Question 30 of 30
Why the Other Options Are Wrong
Correct answer: D
A
Eriochrome black T
Why (D) is the key — Methylene blue is a redox indicator (blue ⇌ colourless leuco form). Eriochrome black T is a metal-ion indicator; methyl orange and phenolphthalein are acid–base indicators.
B
Methyl orange
Ruled out: Using %T in place of absorbance; confusing equivalence point with end point.
C
Phenolphthalein
Ruled out: Isocratic elution = constant mobile phase; gradient = composition changes with time.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427
Q30 · Distractor Analysis

## Slide 82
TOPIC REVISION
Analytical Chemistry (Inorganic) – General
30 PYQs · Last-minute revision
TOPIC SUMMARY
Quantitative methods: titrimetry (equivalence vs end point, indicators), gravimetry, Beer–Lambert spectrophotometry (A = εcl), chromatography (retention, resolution), electrochemical sensors.
IMPORTANT FORMULA SHEET
A = εcl = −log T
Resolution Rs = 2(t₂−t₁)/(w₁+w₂)
N = 16(t_R/w)²; H = L/N
Standard addition for matrix effects
FREQUENTLY ASKED CONCEPTS
Beer's law limits
Chromatographic resolution and plate number
Choice of indicator
Detection limit (3σ)
COMMON MISTAKES & QUICK NOTES
Watch out:
Using %T in place of absorbance; confusing equivalence point with end point.
Isocratic elution = constant mobile phase; gradient = composition changes with time.
MOST-REPEATED PYQs & EXPECTED IN EXAM
PYQs in this topic: Q1 Q2 Q3 Q4 Q5 Q6 Q7 Q8 Q9 Q10 Q11 Q12 Q13 Q14 …
Expect 2 question(s) next session on Analytical Chemistry (Inorganic) – General.
( Mr. Aniket Bhardwaj By ABC Chemistry ) · www.abcchemistry.com · 9212142427

## Slide 83
FOR STUDENTS AND EDUCATORS
Government Jobs and Examination News
Keep track of every notification in one place.
Government Jobs
Latest vacancies
By category
By state
Exams
Chemistry jobs
Government Jobs Blog
Scan to Explore
4ab.in/government-jobs
Examination News
Latest updates
Exam calendar
Admit cards
Results
UG entrance exams
PG entrance exams
NET, SET & PhD exams
School board exams
Examination News Blog
Scan to Explore
4ab.in/examination-news
Vacancies, admit cards, results and exam dates: all in one place
( Mr. Aniket Bhardwaj By ABC Chemistry ) | 4ab.in/educators | @abcchemistry24 | 9212142427

## Slide 84
FOR EDUCATORS
Teach from the Question Bank, one question at a time
Find the right questions, teach them in class, then take them with you.
1 Find questions
Browse
Question search
Topic packs
2 Teach one by one
Question Bank
Show each question to students on the board, in your own order.
3 Export
PPTX, DOCX, PNG (zip), HTML, Markdown
Take the paper home after class.
My papers
Social groups
Question Paper Analyser
AI question paper generator
Paid
Scan to open Question Bank
4ab.in/educators/?m=qb
Many more coming soon
Lifetime free for educators, except AI tools
( Mr. Aniket Bhardwaj By ABC Chemistry ) | 4ab.in/educators | @abcchemistry24 | 9212142427

## Slide 85
TUTOR-BRANDED TEACHING TOOLS
Free whiteboard for educators
Teach on a long whiteboard, your own PDF or photo, or from the question bank.
Whiteboard
PDF
Photo
Question Bank
Start teaching
4ab.in/educators
Need more room? Add more space to the board as you teach.
Tutor pages show a small "Powered by 4AB" line. Premium removes it.
( Mr. Aniket Bhardwaj By ABC Chemistry ) | 4ab.in/educators | @abcchemistry24 | 9212142427

## Slide 86
EXPLORE AND USE
Chemistry Labs: symmetry and crystals
Scan a code or click a card to open the tool.
Molecular Symmetry
Explore molecular symmetry
4ab.in/molecular-symmetry/
Molecular Point Groups
Learn molecular point groups
4ab.in/molecular-point-groups/
Crystal Structure
Explore crystal structures
4ab.in/crystal-structure/
Crystal Space Groups
Browse crystal space groups
4ab.in/crystal-space-groups/
( Mr. Aniket Bhardwaj By ABC Chemistry ) | 4ab.in/educators | @abcchemistry24 | 9212142427

## Slide 87
EXPLORE AND USE
Chemistry Labs: elements, calculation and drawing
Scan a code or click a card to open the tool.
Periodic Table
Explore the elements
4ab.in/periodic-table/
Chemistry Calculator
Solve chemistry calculations
4ab.in/chemistry-calculator/
Chemistry Typing
Type chemistry text
4ab.in/chemistry-typing/
Structure Editor
Draw structures
4ab.in/educators/draw/
( Mr. Aniket Bhardwaj By ABC Chemistry ) | 4ab.in/educators | @abcchemistry24 | 9212142427

## Slide 88
Explore free educator tools
Mr. Aniket Bhardwaj
ABC Chemistry
9212142427
4ab.in/educators
Scan to explore
@abcchemistry24 · Instagram · YouTube · Facebook
( Mr. Aniket Bhardwaj By ABC Chemistry ) | www.abcchemistry.com | 4ab.in/educators | 9212142427